## Slide 1: Credit-Scheduled Delay-Bounded Congestion Control for Datacenters
Inho Cho, Keon Jang*, Dongsu Han
ACM SIGCOMM 2017
*
Notes: Hi, today I will talk about a new credit-based congestion control designed for datacenter.
I am presenter Inho Cho from KAIST and this work is collaborated with Google.

## Slide 2: Datacenter Network
Small Latency
High Bandwidth
Shallow Buffer
Large Scale
< 100
10/40 ~ 100 Gbps
< 30 MB for ToR
> 10,000 machines
1
Notes: Datacenter networks have very different environment compared to Internet or Enterprise network.
It has small latency, high bandwidth, and shallow buffer.
In addition, the scale of datacenter can be huge with tens of thousand machines in a single datacenter.

## Slide 3: Datacenter Network
Small Latency
High Bandwidth
Shallow Buffer
Large Scale
< 100
10/40 ~ 100 Gbps
< 30 MB for ToR
> 10,000 machines
Congestion control is more challenging in datacenter.
1
Notes: 1. These characteristics pose interesting challenges for congestion control as evidenced by many prior works.

## Slide 4: Challenge with small BDP
BDP*(100, 40Gbps) 300 MTUs
…
…
window 1
window 1
window 1
Receiver
Switch
2
* BDP: Bandwidth-delay Product
N Senders
Notes: First, despite of high bandwidth of 10 or even 100 Gbps, bandwidth-delay product is very small due to the tiny latency.
For example, a network with 100us latency and 40Gbps bandwidth has BDP of only 300 MTU sized packets.
This is especially problematic for incast traffic where thousands of flows are competing in the same bottleneck with short burst.
In this scenario, when in-cast happens with more than 300 flows, even window size of one MTU for a flow can exceed the link capacity and build up the queue.

## Slide 5: Rate-based CC + incast traffic
…
…
Switch
3
C/N
C/N
C/N
Receiver
N Senders
Queueing up to N-1!
Number of flows
Queue
…
…
Notes: One might think that if we do congestion control better, this might be solved.
However, this is not the case for incast.
Even if the senders know its exact fair-share rate, in the worst case, packets from all senders can arrive at the switch at the same time and build up the queue.

## Slide 6: Rate-based CC + incast traffic
…
…
Switch
3
C/N
C/N
C/N
Receiver
N Senders
Queueing up to N-1!
Number of flows
Queue
…
…
Notes: One might think that if we do congestion control better, this might be solved.
However, this is not the case for incast.
Even if the senders know its exact fair-share rate, in the worst case, packets from all senders can arrive at the switch at the same time and build up the queue.

## Slide 7: Rate-based CC + incast traffic
…
…
Switch
3
C/N
C/N
C/N
Receiver
N Senders
Queueing up to N-1!
Number of flows
Queue
…
…
Notes: One might think that if we do congestion control better, this might be solved.
However, this is not the case for incast.
Even if the senders know its exact fair-share rate, in the worst case, packets from all senders can arrive at the switch at the same time and build up the queue.

## Slide 8: Rate-based CC + incast traffic
Chart: Number of Flows
| 32 | 64 | 128 | 256 | 512 | 1024 | 2048
min | 0.001 | 0.001 | 0.001 | 0.001 | 1 | 0.001 | 0
q1-min | 1 | 2.5 | 12.5 | 36.5 | 82.5 | 181 | 373.5
median-q1 | 4 | 12.5 | 23.5 | 48.5 | 97.5 | 194 | 385.5
q3-median | 6 | 12.5 | 25 | 49 | 95.5 | 192 | 385.5
max-q3 | 6 | 10.5 | 23 | 46 | 93.5 | 189 | 377.5
4
max
75%-ile
median
25%-ile
min
Total buffer of Trident+
Notes: To demonstrate this, we did a simple experiment using fat-tree topology.
A client sends requests to many servers simultaneously and receives the responses from them repeatedly.
We set the servers to rate-limit their response at the exact fair-share of the bottleneck link capacity.
Here, I’m showing the distribution of queue length with varying number of flows.
[click]
As you can see, even when each server knows the exact fair-share rate, the queue still grows as the number of flow increases.

## Slide 9: Rate-based CC vs. credit-based CC
Chart: Number of Flows
| 32 | 64 | 128 | 256 | 512 | 1024 | 2048
min | 0 | 0 | 0 | 0 | 0 | 0 | 0
q1-min | 63 | 138 | 245 | 508 | 1029 | 3103 | 6213
median-q1 | 9 | 1 | 1 | 1 | 441 | 2 | 15
q3-median | 11 | 2 | 1 | 252 | 14 | 2 | 4
max-q3 | 76 | 123 | 400 | 679 | 1318 | 1504 | 2416
Chart: Number of Flows
| 32 | 64 | 128 | 256 | 512 | 1024 | 2048
min | 0 | 0 | 0 | 0 | 0 | 0 | 0
q1-min | 1 | 2 | 2 | 3 | 4 | 5 | 4
median-q1 | 1 | 1 | 1 | 1 | 0 | 1 | 1
q3-median | 1 | 2 | 2 | 2 | 2 | 2 | 2
max-q3 | 1 | 1 | 2 | 3 | 5 | 4 | 6
Maximum Bound | 35 | 35 | 35 | 35 | 35 | 35 | 35
Total buffer of Trident+
DCTCP
Credit-based Approach
5
Notes: [click]
If we use real protocols such as DCTCP, queuing becomes much worse by factor of 10 or more.
It can fill up the entire buffer in the switch with two thousand flows.
The right figure shows result of our credit-based approach.
[click]
It achieves low and bounded queuing with incast traffic regardless of the number of flows.
Now, let’s take a closer look at how we do this.

## Slide 10: Prior Work with Bounded Queue
Credit-based Flow Control
Centralized
PFC
InfiniBand
ATM Network
PCI Express
RoCE/DCQCN
FastPass
Bounded queue
Bounded queue
Bounded queue
6
Notes: Here, we classify prior works that provide bounded queue into three different categories.
First is Hop-by-hop credit-based flow control, which is used in Infiniband, ATM network, and PCI Express.
And the priority-based flow control (PFC) used in RoCE and DCQCN.
And the centralized packet scheduling used in FastPass.
They all provides bounded queue, but each has its own limitations.

## Slide 11: Prior Work with Bounded Queue
Credit-based Flow Control
Centralized
PFC
InfiniBand
ATM Network
PCI Express
FastPass
Does not scale to datacenter
Requires switch support
Head of line blocking
Possible deadlock
Hard to scale
Global time sync
Single point of failure
Bounded queue
Bounded queue
Bounded queue
6
RoCE/DCQCN
Notes: Credit-based flow control can scale to some extent but it does not scale to datacenter size due to its virtual channel setup cost.
In addition, it requires switch support to generate credits and maintain per-channel state, which can be more expensive than Ethernet.
PFC suffers from head of line blocking and it can have deadlock if you try to scale to more than a single switch.
Centralized packet scheduling is even more difficult to scale and has single point of failure.

## Slide 12: Prior Work with Bounded Queue
Credit-based Flow Control
Centralized
PFC
InfiniBand
ATM Network
PCI Express
FastPass
Does not scale to datacenter
Requires switch support
Head of line blocking
Possible deadlock
Hard to scale
Global time sync
Single point of failure
Bounded queue
Bounded queue
Bounded queue
6
RoCE/DCQCN
How can we get the benefits of credit-based flow control on Ethernet?
Notes: 1. Among those approaches, we are inspired by hop-by-hop credit-based flow control and we asked a question.
2. Can we get the benefits of credit-based flow control on the Ethernet, without hop-by-hop flow control?

## Slide 13: Goal & Our Approach
Proactive end-to-end credit-based congestion control using unreliable credits.
7
ExpressPass
Goal
To achieve bounded queue even with heavy incast using Ethernet switches.
Notes: As an answer of the question, we propose an end-to-end credit-based congestion control which behaves proactively.
It can work on Ethernet switches using unreliable credits.
And we named it ExpressPass.
There are two key differences between hop-by-hop credit-based flow control and our approach.
first, our approach is end-to-end, and second we assume our unreliable credits would be dropped.
As a result we do not require switch support when deploying our solution.
[pause for 2sec]
Now, I’ll show how ExpressPass works.

## Slide 14: ExpressPass End host behavior
Receiver
Sender
I need credit!
8
Credit Request
Credit
Data
Credit Stop
Notes: 1. First, when sender has data to transmit, it transmits a “credit request” signal to the receiver.

## Slide 15: ExpressPass End host behavior
Receiver
Sender
8
Credit Request
Credit
Data
Credit Stop
Notes: 1. Upon receiving the “credit request”, receiver actively generates credits which are minimum sized Ethernet frame, towards the sender.

## Slide 16: ExpressPass End host behavior
Receiver
Sender
No more
!
8
Credit Request
Credit
Data
Credit Stop
Notes: Once the sender receives the credit, it sends one data packet for one credit received.
If there is no available data to send, the credit is discarded immediately.

## Slide 17: ExpressPass End host behavior
Receiver
Sender
stop credit!
8
Credit Request
Credit
Data
Credit Stop
Notes: Finally, when the sender has no more data to send, it transmits “credit stop” signal to the receiver.
Then the receiver stops generating credits.
So far, I explained the end host behavior for the single flow case.
Now let’s see the switch behavior with multiple flows competing in the same bottleneck.

## Slide 18: ExpressPass Switch behavior
Receivers
Senders
9
Credit
Data
Notes: Here, I’m showing the two sender and two receivers sharing a bottleneck in dumbbell topology.
[click]
In ExpressPass, we separate the credit queue and data queue in the switch.
[pause]
Then the switch throttles credit packets.
Throttling rate is determined by the ratio of the credit size and the maximum data size.
This is about 5% of the link capacity in the Ethernet.

## Slide 19: ExpressPass Switch behavior
Receivers
Senders
9
Switch throttles credits.
(Throttling rate 5 %)
Credit
Data
Notes: Here, I’m showing the two sender and two receivers sharing a bottleneck in dumbbell topology.
In ExpressPass, we separate the credit queue and data queue in the switch.
[pause]
Then the switch throttles credit packets.
Throttling rate is determined by the ratio of the credit size and the maximum data size.
This is about 5% of the link capacity in the Ethernet.

## Slide 20: ExpressPass Switch behavior
Switch forwards the data symmetric to the credit.
Receivers
Senders
9
Credit
Data
Notes: For the returning data packet, switch forwards it through the same link as the credit but in the reverse direction.
There are several ways to implement this path symmetry property including the DRILL of the previous talk.

## Slide 21: Credit-scheduled data transmission
…
…
Receiver
Switch
Senders
10
Credit
Data
Number of flows
Queue
Notes: Because switch throttles the credits to ensure no more returning data packets than it can forward, data packet never overflow the link capacity, regardless of the number of flows competing at the bottleneck.
In addition, credit packets naturally schedule the data packet transmissions and removes burst, [pause 1sec] because credits are serialized at the switch.
Therefore, our credit-based congestion control can achieve zero queuing in ideal condition.
However, this approach that I just described has some challenges in practice.

## Slide 22: Challenges
Challenges | Techniques to address
Signaling overhead | Piggybacking to handshake packets
Non-zero queueing | Bounded queue
Credit waste | Credit feedback control
Fair drop on switch | Jitter, variable-sized credits
Path symmetry | Deterministic ECMP, packet level load balancing
Multiple traffic classes | Prioritizing credits rather than data
11
Notes: Due to the time limitation, I will not cover all of these in this talk and I will talk about three challenges:
signaling overhead, non-zero queueing, and credit waste.

## Slide 23: Signaling Overhead
Receiver
Sender
I need credit!
12
Credit Request
Credit
Data
Credit Stop
Notes: First, there is signaling overhead of one RTT in the beginning.
However, if the flow uses non-persistent connection, we can piggyback it into the handshake packets.
Even with persistent connection, the cost of one RTT should be very cheap because credit-based approach can provide low and bounded queuing and the latency is very short in datacenter.

## Slide 24: Maximum Bound of Data Queue
13
Credit
Data
Receiver
Sender 1
Sender 2
Sender 3
Notes: Second challenge is that even with credit-based approach, queue build-up can still occur.
It can achieve zero queuing if the delays from the departure of the credit to the arrival of the data at a switch port are always the same.
However, in real datacenter topology, different paths can have different delays depending on number of hops, queueing delay, and host delay.

## Slide 25: Maximum Bound of Data Queue
delay = 1
delay = 2
delay = 3
13
Credit
Data
Receiver
Sender 1
Sender 2
Sender 3
Notes: 1. Let’s consider the scenario where each path has delay of 1, 2, and 3.

## Slide 26: Maximum Bound of Data Queue
13
Credit
Data
Receiver
Sender 1
Sender 2
Sender 3
Queuing!
Notes: In the worst case, if the receiver send credits in the order of the sender 3, 2 and 1, returning data packets from different paths arrives at the switch at the same time and queue length can grow up.
However, the maximum queue occupancy is still bounded by the difference between the maximum and the minimum delay regardless of the traffic.
Then what is the maximum bound for realistic datacenter topology?

## Slide 27: Maximum Bound of Data Queue
14
Chart: 
| 10 | 40 | 100
Max. Bound (Software) | 8.9289 | 16.2681 | 31.2688
Max. Bound (Hardware) | 4.3981 | 7.8686 | 14.8095
Buffer of Brodcom chip | 9 | 12 | 16
…
…
…
…
* Trident+ (10G), Trident II (40G), Tomahawk (100G)
Notes: Using Network Calculus, we calculate the worst case queue length in 32-ary fat-tree topology with 8,192 nodes.
We assume that all the link delay is 5us, which is conservative estimate.
The right figure shows maximum queue bound of software and hardware implementation and actual buffer space provided by Broadcom chips at the ToR switch.
The difference between software and hardware is that they have different delay variation from the receipt of credits to the departure of the data.
 Continued.

## Slide 28: Maximum Bound of Data Queue
14
Chart: 
| 10 | 40 | 100
Max. Bound (Software) | 8.9289 | 16.2681 | 31.2688
Max. Bound (Hardware) | 4.3981 | 7.8686 | 14.8095
Buffer of Brodcom chip | 9 | 12 | 16
…
…
…
…
* Trident+ (10G), Trident II (40G), Tomahawk (100G)
Notes: Compared to the buffer space in Broadcom chips, software implementation of ExpressPass requires more buffer in 40 and 100 Gbps.
However, the maximum bound here is assuming the worst case which is unlikely to happen.
With less buffer than the bound, it can still operate with possible data loss and retransmission.
For hardware implementation, ExpressPass has maximum bound lower than the buffer space of available Broadcom chip.

## Slide 29: Credit Waste
Receiver
Sender
No more
!
15
Credit Request
Credit
Data
Credit Stop
Notes: Another challenge is the credit waste.
Credits can be wasted for two reasons.
If the sender has slower data generation rate than credit arrival rate, some credits can be wasted in the middle of the flow.
In addition, because receiver keeps generating credits until it gets the “credit stop” signal, the sender may get credits with no data available to send at the end of the flow.
Such a credit waste can result in under-utilization of the network which could have been used by other flows that has data to send.
 Continued.

## Slide 30: Credit Waste
Receiver
Sender
No more
!
15
Credit Request
Credit
Data
Credit Stop
Notes: We can reduce the credit waste at the end of the flow by estimating the number of credits to receive remaining data packets assuming it knows the flow size in advance.
To minimize the credit waste in the middle of the flow due to sender’s slow data generation, we adjust credit sending rate through the feedback control at the receiver-side, using the number of credit sent and the number of data received.
Then how is it different from the traditional feedback control on data?

## Slide 31: Credit Feedback Control
Proactive Congestion Control
Prevents the congestion before actual congestion happens using credits.
time
rate
16
Cheap credit drop
We can increase rate aggressively.
Bandwidth probing is cheap.
Convergence can be faster.
Notes: Above all, credit feedback control triggers before actual data congestion happens.
In other words it prevents congestion proactively.
This is different from feedback control on data which reacts to the congestion after it happened.
In addition, because credit drop has little cost, credit feedback control can increase the rate aggressively without worrying about the data loss.
In our implementation, we use the variation of binary search increase where the new rate is weighted average of the current rate and the maximum rate.

## Slide 32: Credit Feedback Control
Receivers
Senders
16
Credit
Data
Notes: Even when credit feedback control over-estimate the fair-share rate, it does not incur any data congestion because switch throttles the credits.
On the other hand, if data feedback control over-estimate the fair-share rate, it will incur data congestion and start to build up the queue and potentially drop the packets.

## Slide 33: Credit Feedback Control
Proactive Congestion Control
Prevents the congestion before actual congestion happens using credits.
time
rate
16
Credit drop is Cheap
Makes bandwidth probing cheap.
Can increase rate aggressively.
Converges faster.
Notes: Thanks to the aggressive rate increase, credit feedback control converges faster.
This is the high level description of our credit feedback control mechanism and the detailed algorithm and the stability analysis are included in the paper.

## Slide 34: Credit Waste & Convergence Time
Chart: 
 | 2 | 3 | 4 | 5 | 6 | 14
More
Aggressive
Less
Aggressive
Convergence Time
Chart: 
 | 80 | 40 | 20 | 10 | 4 | 2
More
Aggressive
Less
Aggressive
Level of Aggressiveness
Level of Aggressiveness
17
Credit Waste
time
time
rate
rate
Notes: With the credit feedback control, we can reduce the credit waste, but there exists the trade-off between credit waste and fast convergence depending on the aggressiveness of the rate increase.
[click]
To quantify the trade-off, we measure the credit waste of the single packet flow and the convergence time of the two flows varying the aggressiveness of the binary search increase with different weights.
[click]
As shown in the figures, less aggressive increase can reduce the credit waste while sacrificing the convergence time.
On the other hand, more aggressive rate increase can reduce the convergence time, but it leads to large credit waste.

## Slide 35: Credit Waste & Convergence Time
Chart: 
 | 2 | 3 | 4 | 5 | 6 | 14
More
Aggressive
Less
Aggressive
Convergence Time
Chart: 
 | 80 | 40 | 20 | 10 | 4 | 2
More
Aggressive
Less
Aggressive
Level of Aggressiveness
Level of Aggressiveness
17
Credit Waste
Notes: For the evaluation, we use the second least aggressive value in this figure.

## Slide 36: Evaluation Setup
Testbed setup
  Dumbbell topology
  Implementation on SoftNIC
  12 hosts (Xeon E3/E5) connected to single ToR (Quanta T3048)
  Each host has 10Gbps x 1port
NS-2 Simulation Setup
  Fat-tree topology
  192 hosts / 32 ToR / 16 aggr. / 8 core switches
  Each host has 10Gbps x 1port
18
Notes: To evaluate ExpressPass, we constructed a testbed with SoftNIC implementation.
We could configure the credit throttling using maximum bandwidth metering feature in the Brodcom chip.
[pause]
We used ns-2 simulation for large scale evaluation of realistic workloads and compared it against other congestion controls.
We use non-persistent connection for the simulation.

## Slide 37: Evaluation
Does ExpressPass provides low & bounded queueing with realistic workloads?
Is the convergence fast and stable?
How low & bounded queuing and fast & stable convergence translate into the flow completion time?
19
Notes: Throughout the evaluation we answer the three questions.
Does ExpressPass provides low & bounded queueing with realistic workloads?
Is the convergence fast and stable?
How low & bounded queueing and fast & stable convergence translate into flow completion time?

## Slide 38: Realistic Workloads
 | Data Mining | Web Search | Cache Follower | Web Server
0 – 10KB (S) | 78% | 49% | 50% | 63%
10 – 100KB (M) | 5% | 3% | 3% | 18%
100KB–1MB (L) | 8% | 18% | 18% | 19%
1MB- (XL) | 9% | 20% | 29% | -
Average flow size | 7.41MB | 1.6MB | 701KB | 64KB
20
Notes: For realistic workloads for large scale simulation, we use four different workloads which have various average flow sizes.
We categorized the flows of each workload into four different classes based on the flow sizes.

## Slide 39: Realistic Workloads
 | Data Mining | Web Search | Cache Follower | Web Server
0 – 10KB (S) | 78% | 49% | 50% | 63%
10 – 100KB (M) | 5% | 3% | 3% | 18%
100KB–1MB (L) | 8% | 18% | 18% | 19%
1MB- (XL) | 9% | 20% | 29% | -
Average flow size | 7.41MB | 1.6MB | 701KB | 64KB
20
Notes: Throughout this talk we will focus on cache follower workload.
Among cache follower workload, we will pay attention to the smallest flow group and the largest flow group.
The reason is that they’re the dominant fraction of traffic and highlight the trade offs of ExpressPass well.
The overall trend is similar in other workloads, and the paper contains the more results.

## Slide 40: Bounded Queue cache follower workload / load 0.2 – 0.4 / 0KB ~ (All Size)
Chart: Load
| 0.2 | 0.4 | 0.6
DCTCP | 153.8 | 178.3 | 214.7
Chart: Load
| 0.2 | 0.4 | 0.6
Xpass | 34 | 41.78 | 32.3
ExpressPass
DCTCP
21
Notes: One of strong benefits of our approach is bounded queue regardless of the traffic load.
To verify this, we run cache follower workload with three different loads and measure the maximum queue length during the whole experiment.
Those figures show that in our approach, maximum queue length does not increase even with larger load while in DCTCP maximum queue length grows as the load increases.
For the detailed analysis on the bounded queue property, please refer to the paper.
Now, how much queue is occupied on average and on maximum compared with other congestion controls?

## Slide 41: Low Average Queue cache follower workload / load 0.6 / 0KB –
22
Chart: Average Queue
| X-Pass | RCP | DCTCP | DX | HULL
Average | 0.5 | 14.58 | 6.18 | 0.77 | 0.82
Chart: Max. Queue
| X-Pass | RCP | DCTCP | DX | HULL
99-ile | 32.3 | 375.3 | 214.7 | 39.3 | 79.28
Notes: This two figures show average and maximum queue length of cache follower workload with load 0.6.

## Slide 42: Low Average Queue cache follower workload / load 0.6 / 0KB –
Chart: Average Queue
| X-Pass | RCP | DCTCP | DX | HULL
Average | 0.5 | 14.58 | 6.18 | 0.77 | 0.82
Chart: Max. Queue
| X-Pass | RCP | DCTCP | DX | HULL
99-ile | 32.3 | 375.3 | 214.7 | 39.3 | 79.28
x29
x12
x1.5
x1.6
x12
x6.6
x1.2
x2.5
22
539.2
Bound
Notes: Among different congestion controls, ExpressPass has least average and maximum queuing.
Compared with the maximum bound, it occupies the maximum queue of only 6% of the bound.
DX and HULL are also optimized for low queuing, and they show the small queue occupancy compared with RCP and DCTCP.

## Slide 43: Fast & Stable Convergence
Chart: Time (ms)
Chart: Time (us)
ExpressPass
DCTCP
23
Notes: Next, to see how fast it converges and whether it is stable after convergence, we injected a new flow while a link is fully occupied by another flow and measure the convergence time in the testbed.
ExpressPass took 100us to converge while DCTCP took 70ms.

## Slide 44: Fast & Stable Convergence
Chart: Time (ms)
Chart: Time (us)
ExpressPass
DCTCP
x700
23
Notes: The convergence time of our approach is 700 times faster than DCTCP.
I’d like to note that we took average of 25us for single data point in ExpressPass while we took average of 10ms for single data point in DCTCP.
If we use the 10ms average for ExpressPass, then it is much more stable than DCTCP.

## Slide 45: Flow Completion Time cache follower workload / load 0.6 / 0 – 10KB
Chart: Average FCT
| X-pass | RCP | DCTCP | DX | HULL
 | 0.10914 | 0.93782 | 0.27835 | 0.13183 | 0.13261
Chart: 99%-ile FCT
| X-pass | RCP | DCTCP | DX | HULL
 | 0.14486 | 3.5355 | 0.46977 | 0.17117 | 0.18339
24
Notes: Finally, how low & bounded queuing and fast & stable convergence translate into the flow completion time?
The two figures show average and 99%-ile flow completion time of short flows which is less than 10KB from cache follower workload with load 0.6.

## Slide 46: Flow Completion Time cache follower workload / load 0.6 / 0 – 10KB
Chart: Average FCT
| X-pass | RCP | DCTCP | DX | HULL
 | 0.10914 | 0.93782 | 0.27835 | 0.13183 | 0.13261
Chart: 99%-ile FCT
| X-pass | RCP | DCTCP | DX | HULL
 | 0.14486 | 3.5355 | 0.46977 | 0.17117 | 0.18339
24
x8.5
x2.5
x1.2
x1.2
x25
x3.4
x1.2
x1.3
Notes: It shows that our approach has the least average and 99%-ile flow completion time.
For the small flows, latency dominates the flow completion time.
For this reason, ExpressPass, DX, and HULL which is optimized for low queueing has shorter flow completion time than RCP or DCTCP.

## Slide 47: Flow Completion Time cache follower workload / load 0.6 / 1MB –
Chart: Average FCT
| X-Pass | RCP | DCTCP | DX | HULL
0.6 | 12.8097 | 13.0297 | 10.8137 | 32.8894 | 55.6626
25
Notes: 1. Then, how well does our approach work in extra large flows?

## Slide 48: Flow Completion Time cache follower workload / load 0.6 / 1MB –
Chart: Average FCT
| X-Pass | RCP | DCTCP | DX | HULL
0.6 | 12.8097 | 13.0297 | 10.8137 | 32.8894 | 55.6626
x1.0
x0.8
x2.6
x4.3
25
Notes: Compared with DCTCP, our approach has longer average flow completion time for extra large flows.
For larger flows, bandwidth impacts the flow completion time more than latency.
There are multiple factors that affects the longer flow completion time for XPass.
First, it reserves the bandwidth for credit which accounts for about 5% of the bandwidth.
Second, by allowing small flow to ramp up quickly, it delays the longer flows.
Third, wasted credits at the receiver or in the network result in under-utilization.
But still, ExpressPass provides the better trade-off between low queuing and high bandwidth compared to DX and HULL.

## Slide 49: Conclusion
ExpressPass is end-to-end, credit-scheduled, and delay-bounded congestion control for datacenter.
ExpressPass propose a new proactive datacenter congestion control.
Our evaluation on testbed and ns-2 simulation show that ExpressPass achieves
  Low & bounded queueing
  Fast & stable convergence
  Short flow completion time especially for small flows
26
Notes: Let me conclude the talk.
ExpressPass is an end-to-end, credit-scheduled and delay-bounded congestion control designed for datacenter.
By controlling the congestion using credits rather than data packet itself, ExpressPass propose a new proactive datacenter congestion control where more aggressive rate increase is possible with little risk of data packet drop.
Our extensive evaluation on the testbed and the simulation shows that ExpressPass achieves low & bounded queueing, fast & stable convergence, and short flow completion time especially for smaller flows.
We believe that ExpressPass can significantly improve the tail latency of latency-sensitive traffics such as user-facing database traffics at the small cost of bandwidth hungry traffic.

## Slide 50: Thanks
Happy to answer your questions
Notes: Thanks for your attention, and I’m happy to answer your questions.
Possible Question
== How is it different from NTP?
The assumptions of NTP and our approach are different. NDP assumes that datacenter provides sufficient cross-sectional bandwidth with perfect load balancing, and there is no congestion in the network core. However we assumes that there might be congestion at the core. If there is congestion in the network core, our approach has faster FCT due to fewer retransmissions. However, if there is no congestion in the network core, we think both will behave the same except for the one RTT signaling overhead in our approach.
In addition, NTP requires switch programmability while our approach can be implemented using commodity Ethernet switches.
== Credit queue
For the simplicity, here we show that credit queue capacity of 2 credits, but for the evaluation we used credit queue capacity of 8 credits. If we use the small credit queue capacity, there can be under-utilization of the network, on the other hand, if we use the large credit queue capacity, the latency will increase.
== How to reduce bandwidth degradation
We can reduce the bandwidth regression in two ways.
more data packets for one credit received.  this will reduce the reserved bandwidth for credits
Less aggressive rate increase in credit feedback control  it will increase the convergence time
== How is it different from pHost?
Tokens in pHost and credits in our approach shares the similar idea, but
pHost assumes full bisection bandwidth with which there is no congestion in the network core while we assume that there might be congestion in the network core.
And pHost focus on flow scheduling at end host scheduling rather than congestion control.
== Why hop-by-hop credit-based flow scheduling is not scalable?
Using hop-by-hop CC requires setting up virtual channels between host pairs. Given N hosts in a datacenter, we might need up to n^2 virtual channels. Even in the best case, if all machines are sending data we should need at least N/2 virtual channels (one for each host pair). This requires a large amount of state on the switches, and does not scale.
== What if your evaluation do use persistent connection?
Then, we will pay one additional RTT as an signaling overhead. I’m sorry, but we don’t have experimental result for that. Considering the link delay is 5us and the average queue is low, one RTT should be less than 100us. Then our approach will take 100us more FCT than other approach.
== Deployment
Credit can be used as an orthogonal signal to other congestion signal such as packet drop, ECN mark, or long delay. By reacting both credits and traditional congestion signal, we can overlay ExpressPass over existing congestion control to deploy.

## Slide 51: Credit Queue Capacity vs. Utilization

## Slide 52: Fairness